## Slide 1: Supervised learning for heartbeat detection in photoplethysmography
Talha Agcayazi
Tanner Songkakul

## Slide 2: Background & Motivation
Photoplethysmography (PPG)
  Works by interaction of photons with oxygenated and deoxygenated hemoglobin
  Heartbeat causes variation of blood volume which can be measured by PPG
  Used for many wearable health sensing applications to measure heart rate (HR)
Commercial fitness trackers demonstrate inaccuracy in HR measurement [1]
  Low Signal to Noise Ratio
  Motion Artifacts
LED
Photodiode

## Slide 3: Machine Learning for PPG HR Detection
Our approach: use supervised learning to detect heartbeats from PPG signals (Inspired by Grisan et. Al [2])
  Import data from TROIKA Dataset [3]
  Preprocess PPG data
  Identify ground truth heartbeats from ECG data
  Extract features from PPG data
  Apply various classifiers to distinguish heartbeat from non-heartbeat
  Compare results to CNN
Notes: Need to establish that we are doing HB vs No HB distinction for HRate

## Slide 4: TROIKA Dataset [3]
  Contains 2 channels PPG, electrocardiogram (ECG), and accelerometer data from 12 patients, all sampled at 125 Hz
  Walked or ran on a treadmill at speeds of 1–2 km/h, 6–8 km/h, and 12–15 km/h,
  Encouraged to pull clothes, wipe sweat on forehead, and push buttons on the treadmill.
PPG and ECG Data for one patient, full trial
PPG and ECG Data for one patient, 10 sec window

## Slide 5: Preprocessing PPG Signal
  Find average and standard deviation of windows of L=FsN. We chose N=8, so L=1000
  Normalize using
  Find trend of PPG data with a moving average filter of L=FsN, N=2, L=250.
  Detrend PPG data by subtracting trend from normalized PPG data
  Apply 7th order Butterworth Filter, Fc=18Hz

## Slide 6: Preprocessing Results

## Slide 7: Ground Truth Extraction- Peak Detection
  Used Pan-Tompkins Algorithm to extract peak locations from ECG data

## Slide 8: Ground Truth Extraction- HB vs NHB Segmentation
  Extract PPG segments corresponding with heartbeat (HB) using locations from ECG signal starting at HB location Ri and spanning
  Extract PPG segments corresponding with non-heartbeat (NHB) using locations from the ECG signal offset by half of a beat duration
  Resize HB and NHB segments to max segment size lseg=140 by stretching and interpolation
  16K HB and NHB segments each

## Slide 9: Ground Truth Extraction- Results
ECG
PPG
Samples
Samples
HB Segments
NHB Segments

## Slide 10: Feature Extraction
  Extract 302 features for each segment and label HB/NHB:
  Segment samples themselves (140 features)
  Mean and standard deviation (2 features)
  3 level quantized version of segment: -1 for , +1 for , 0 otherwise (140 features)
  12 PCA coefficients (12 features)
  Position of maximum and minimum intensity values of segment (2 features)
  Time difference between locations containing maximum and minimum intensity values (1 features)
  Segment energy in [0.04, 0.09], [0.09,0.15],[0.15,0.60] Hz bands (3 features)

## Slide 11: Machine Learning Techniques
  Conventional Techniques
    Linear Discriminant
    K-Nearest Neighbors (K-NN)
    Decision Tree
    Support Vector Machine (SVM)
  Convolutional Neural Network
    Convolutional Neural Networks (CNN)

## Slide 12: Conventional Classification Results
Classifier | Accuracy
Linear Discriminant | 80.6%
1-NN | 81.1%
5-NN | 83.5%
Decision Tree | 80.5%
Linear SVM | 79.2%
Cubic SVM | 84.5%
  Implemented with Matlab’s Classification Learner App
  5-fold validation
  Used all 302 features

## Slide 13: Convolutional Neural Network Structure
  Input: Segment samples only
  Kernel: 3x1
  Activation: Relu
  Dropout: 0.5
  Pool Size: 2
  Output: 2 classes (softmax)
140x1

## Slide 14: CNN Results
Chart: Accuracy vs Epoch #
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Accuracy | 0.8094 | 0.8347 | 0.8434 | 0.8464 | 0.8525 | 0.856 | 0.8571 | 0.8631 | 0.8642 | 0.8666
Classifier | Accuracy
Cubic SVM (302 features) | 84.5%
CNN (No features) | 86.6%

## Slide 15: Conclusions
  Preprocessing, ground truth extraction, and future extraction from PPG and ECG signals
  Compared conventional and neural network classifiers
  Achieved a peak performance of 86% correct heartbeat identification without any feature engineering

## Slide 16: Future Work
  Try a variety of hyperparameters for CNN
  Incorporate more PPG/ECG data
  Incorporate accelerometer data for adaptive filtering
  Perform PCA on all features and remove some of the unnecessary ones
  Try extra features like: wavelet and coefficient of skewness
  Incorporate classification results into real time systems for physiological health monitoring

## Slide 17: Sources
  [1] S. Benedetto, C. Caldato, E. Bazzan, D. C. Greenwood, V. Pensabene, and P. Actis, “Assessment of the Fitbit Charge 2 for monitoring heart rate,” PLoS One, vol. 13, no. 2, pp. 1–11, 2018.
  [2] E. Grisan, G. Cantisani, G. Tarroni, S. K. Yoon and M. Rossi, “A supervised learning approach for the robust detection of heart beat in plethysmographic data”; 2015 37th Annual International Conference of the IEEE Engineering in Medicine and Biology Society (EMBC), Milan, 2015, pp. 5825-5828.
  [3] S. Zhu, K. Tan, X. Zhang, Z. Liu, and B. Liu, “TROIKA: A mixed approach for heart rate monitoring during intensive physical exercise using wrist-type PPG Signals,” Proc. Annu. Int. Conf. IEEE Eng. Med. Biol. Soc. EMBS, vol. 2015–Novem, no. 2, pp. 2347– 2350, 2015.